## Slide 1: Fractal Analysis of Particle Contour

## Slide 2: Gamma Correction
Uncorrected Image Corrected Image (Gamma = 2.2)
The Gamma correction method makes an image brighter which makes it easier to differentiate between the foreground and background.
The method is done by rescaling the pixel intensity from between 0 and 255 to 0 and 1. After rescaling the pixels, raise it to the power of 1/gamma where if gamma is lower than 1 it makes the image darker and if gamma is higher than 1, it makes it brighter. Then we rescale it back up to 0 to 255

## Slide 3: Otsu’s Method
= between class variance or the differentiation between the foreground and background
To calculate Wb, Wf, Ub and Uf we use the following formula :-
Wb = (number of pixels in background)/total pixels
Wf = (number of pixels in foreground)/total pixels
Ub = (sum for all I from 0 to assumed threshold(number of pixels in intensity I * I))/total pixels in background
Uf = (sum for all I from assumed threshold to 255 (number of pixels in intensity I * I))/total pixels in foreground

## Slide 4
Otsu’s Method

## Slide 5
Otsu’s Method

## Slide 6
Otsu’s Method

## Slide 7: Binarizing image

## Slide 8
Binarizing image

## Slide 9: Finding contours
All boundaries of all particles in image
Isolating the main boundary required by finding the largest boundary

## Slide 10: Fractal Analysis
Find area of particle
Find circle with same area
Initial stick length is diameter of this circle
Multiply by 1.0816 because 1.04 is the mm to pixel ratio in the resolution of the image

## Slide 11: Fractal Analysis
A
B
B
B
B
A
B
B
B
B

## Slide 12: Fractal Analysis
Now find the perimeter again by taking the next point on the contour as your initial point
Keep finding perimeters for all points on contour as initial point
The perimeter we consider for this stick length is the smallest calculated perimeter

## Slide 13: Fractal Analysis
Repeat the whole process but take a smaller stick length
After each perimeter calculation, store the perimeter/diameter value and the ratio between the current stick length and the initial diameter calculated
Stop the process once the perimeter stops increasing and becomes constant

## Slide 14: Different approaches
While the original paper tells us to take the minimum of the perimeters calculated, another paper in the references tells us to take the average. Here are both compared

## Slide 15: Fractal Analysis
Create a scatterplot of all points on a log-log graph with the B/D as the X value and the P/D as the Y value
Graph from paper
Graph from code

## Slide 16: Linear regression
Select points on the graph to draw linear regressions between. The code will give you the R-Squared value of the lines and if it is unideal, select the points again to create different linear regressions.

## Slide 17: Interpreting the data
From the graph, we say that the slope of the right line is an indicator of the angularity(m) and the slope of the left line is an indicator of its particle roughness(u).
To determine the overall form(M) of the particle, we compare it to a circle to get a quantitative value. We first use the below formula for both a circle and the observed particle to get 2 values
We then divide the circle’s value by the particle’s value which gives us the overall form of the particle.

## Slide 18: Results - Graphs

## Slide 19
Alshibli
DOI
PDF
The first thing we look at is the influence of the resolution i.e., the number of pixels in the image, on the fractal analysis.
The Alshibli image had 695 pixels in its boundary. The DOI image had 795 pixels in its boundary. The PDF image had 905 pixels in its boundary. Hence, despite different resolutions and pixels, the values for all 3 are similar.

## Slide 20
m = 0.05
u = 0.12
M = 0.75
m = 0.07
M = 1.24
m = 0.07
M = 0.78
m = 0.07
M = 0.43

## Slide 21
m = 0.04
u = 0.06
M = 0.96
m = 0.06
u = 0.12
M = 0.84
m = 0.32
M = 0.35
m = 0.02
u = 0.05
M = 0.87
6

## Slide 22
m = 0.05
u = 0.12
M = 0.72
m = 0.06
u = 0.10
M = 0.82
m = 0.05
u = 0.10
M = 0.59

## Slide 23
Material | M (Guida et al. 2019) | M (Present study) | m (Guida et al. 2019 | m (Present Study) | 𝛍 (Guida et al. 2019) | 𝛍 (Present study)
Toyoura Example | 0.75 | 0.75 | 0.04 | 0.05 | 0.13 | 0.12
Circle | 1 | 1.24 | 0.07 | 0.07 | - | -
Square | 0.74 | 0.78 | 0.07 | 0.07 | - | -
Rectangle | - | 0.43 | 0.07 | 0.07 | - | -
Snowflake | - | 0.35 | 0.26 | 0.32 | - | -
ASTM 1 | 0.87 | 0.87 | 0.01 | 0.02 | 0.04 | 0.05
ASTM 2 | 0.84 | 0.84 | 0.03 | 0.06 | 0.12 | 0.12
ASTM 3 | 0.95 | 0.96 | 0.02 | 0.04 | 0.06 | 0.06
Toyoura 1 | 0.76 | 0.72 | 0.05 | 0.05 | 0.11 | 0.12
Toyoura 2 | 0.81 | 0.82 | 0.05 | 0.06 | 0.09 | 0.10
Toyoura 3 | 0.59 | 0.59 | 0.05 | 0.05 | 0.08 | 0.10

## Slide 24: Conclusion
The particle shape characterization has been completed for 11 different particles.
The data collected matches the data from the source paper (Guida et al. 2019)